## Slide 1: CE/CS/TE 4390 Computer Networks
Network Application Programming – An Overview
UT
D
application
transport
network
data link
physical
Adapted from “Computer Networking – a Top-Down Approach”
© 1996-2012 by J.F Kurose and K.W. Ross, All Rights Reserved
Notes: How to write a network app?
What/why/how of sockets?
How multiple net apps in a host is assigned an address?
How to use sockets in a network app using Java?

## Slide 2: Socket Programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 3: Socket Programming
  Two socket types for two transport services:
  UDP: unreliable datagram
  TCP: reliable, byte stream-oriented
  Application example:
Client reads a line of characters (data) from its keyboard and sends the data to the server.
The server receives the data and converts characters to uppercase.
The server sends the modified data to the client.
The client receives the modified data and displays the line on its screen.

## Slide 4: Socket Programming with UDP
UDP: no “connection” between client & server
no handshaking before sending data
sender explicitly attaches IP destination address and port # to each packet
rcvr extracts sender IP address and port# from received packet
UDP: transmitted data may be lost or received out-of-order
Application viewpoint:
UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server

## Slide 5
UDP uses Datagram packets to implement connectionless packet delivery
Java classes are used DatagramPacket and DatagramSocket
  DatagramPacket(byte[] buf, int length, InetAddress address, int port);
Send data: send(DatagramPacket p)
Receive data: receive(DatagramPacket p)

## Slide 6: Client/server Socket Interaction: UDP
close
clientSocket
read datagram from
clientSocket
create socket:
DatagramSocket clientSocket
= new DatagramSocket();
Create datagram with server IP and
port=x; send datagram via clientSocket
create socket, port= x:
serverSocket =
socket(AF_INET,SOCK_DGRAM)
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number
server (running on serverIP)
client

## Slide 7: Example: Java client (UDP)
import java.io.*;
import java.net.*;
class UDPClient {
public static void main(String args[]) throws Exception
{
DatagramSocket clientSocket = new DatagramSocket();
byte[] sendData = new byte[1024];
byte[] receiveData = new byte[1024];
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
String sentence = inFromUser.readLine();
sendData = sentence.getBytes();
InetAddress IPAddress = InetAddress.getByName("hostname");
create
client socket
create
Input stream
translate
hostname to IP
address using DNS

## Slide 8: Example: Java client (UDP) - cont’d
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress, 9876);
clientSocket.send(sendPacket);
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
clientSocket.receive(receivePacket);
String modifiedSentence =
new String(receivePacket.getData());
System.out.println("FROM SERVER:" + modifiedSentence);
clientSocket.close();
}
}
create datagram with data-to-send,
length, IP addr, port
send datagram
to server
read datagram
from server

## Slide 9: Example: Java Server (UDP)
import java.io.*;
import java.net.*;
class UDPServer {
public static void main(String args[]) throws Exception
{
DatagramSocket serverSocket = new DatagramSocket(9876);
byte[] receiveData = new byte[1024];
byte[] sendData = new byte[1024];
while(true)
{
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
serverSocket.receive(receivePacket);
create
datagram socket
at port 9876
create space for
received datagram
receive
datagram

## Slide 10: Example: Java Server (UDP) – cont’d
String sentence = new String(receivePacket.getData());
InetAddress IPAddress = receivePacket.getAddress();
int port = receivePacket.getPort();
String capitalizedSentence = sentence.toUpperCase();
sendData = capitalizedSentence.getBytes();
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress,
port);
serverSocket.send(sendPacket);
}
}
}
get IP addr
port #, of
sender
write out
datagram
to socket
end of while loop,
loop back and wait for
another datagram
create datagram
to send to client

## Slide 11: Socket Programming with TCP
client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact (ServerSocket class)
client contacts server by:
Creating TCP socket, specifying IP address, port number of server process
when client creates socket: client TCP establishes connection to server TCP
when contacted by client, server TCP creates new socket (Socket class) for server process to communicate with that particular client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
  new socket is used to exchange data with the client using input and output streams
TCP provides reliable, in-order
byte-stream transfer (“pipe”)
between client and server
application viewpoint:

## Slide 12: TCP Sockets based client-server programming
Reference Book:
Object-Oriented Programming with Java by Rajkumar Buyya, S Thamarai Selvi, Xingchen Chu

## Slide 13: Client/server Socket Interaction: TCP
wait for incoming
connection request
connectionSocket =
welcomeSocket.accept()
create socket,
port=x, for incoming request:
ServerSocket welcomeSocket = new ServerSocket(6789);
create socket,
connect to hostid, port=x
clientSocket = socket()
server (running on hostid)
client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket

## Slide 14: Example: Java Client (TCP)
import java.io.*;
import java.net.*;
class TCPClient {
public static void main(String argv[]) throws Exception
{
String sentence;
String modifiedSentence;
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
Socket clientSocket = new Socket("hostname", 6789);
DataOutputStream outToServer =
new DataOutputStream(clientSocket.getOutputStream());
create
input stream
create
clientSocket object
of type Socket,
connect to server
create
output stream
attached to socket
This package defines Socket()
and ServerSocket() classes
server port #
server name,
e.g., www.umass.edu

## Slide 15: Example: Java client (TCP) – cont’d
BufferedReader inFromServer =
new BufferedReader(new
InputStreamReader(clientSocket.getInputStream()));
sentence = inFromUser.readLine();
outToServer.writeBytes(sentence + '\n');
modifiedSentence = inFromServer.readLine();
System.out.println("FROM SERVER: " + modifiedSentence);
clientSocket.close();
}
}
create
input stream
attached to socket
send line
to server
read line
from server
close socket
(clean up behind yourself!)

## Slide 16: Example: Java server (TCP)
import java.io.*;
import java.net.*;
class TCPServer {
public static void main(String argv[]) throws Exception
{
String clientSentence;
String capitalizedSentence;
ServerSocket welcomeSocket = new ServerSocket(6789);
while(true) {
Socket connectionSocket = welcomeSocket.accept();
BufferedReader inFromClient =
new BufferedReader(new
InputStreamReader(connectionSocket.getInputStream()));
wait, on welcoming
socket accept() method
for client contact create,
new socket on return
create
welcoming socket
at port 6789
create input
stream, attached
to socket

## Slide 17: Example: Java Server (TCP) – cont’d
DataOutputStream outToClient =
new DataOutputStream(connectionSocket.getOutputStream());
clientSentence = inFromClient.readLine();
capitalizedSentence = clientSentence.toUpperCase() + '\n';
outToClient.writeBytes(capitalizedSentence);
}
}
}
read in line
from socket
create output
stream, attached
to socket
write out line
to socket
end of while loop,
loop back and wait for
another client connection